## Slide 1: EADA Pro - Phase 1 Review
Edge AI for Adaptive TV/Billboard Applications
Intelligent Brightness, Volume & Media Control
October 2025

## Slide 2: Project Overview
Vision: Intelligent, privacy-preserving adaptive system for TV/billboard applications
• Real-time AI adjusts brightness, volume, and media based on audience presence
• Edge-first deployment with computer vision and audio processing
• Privacy-preserving: No data storage, local processing only
• Phase 1 Focus: Core functionality - distance detection, adaptive controls, media pause/resume

## Slide 3: Technical Architecture
Modular Design with Clean Separation of Concerns
Perception Layer:
  • Face Detector (MediaPipe Face Mesh)
  • Face Counter with position tracking
Intelligence Layer:
  • Environment Monitor (ambient light)
  • Audio Analyzer (background music)
Adaptation Layer:
  • Brightness Controller (30-100% range)
  • Volume Controller (20-100% with steep curve)
  • Weighted Adapter (multi-face support)
Core: System Manager orchestrates all modules

## Slide 4: Key Algorithms Implemented
Distance Estimation & Adaptive Control
Distance Calculation:
  • Face width triangulation using MediaPipe landmarks (234-454)
  • Calibrated for accurate real-world measurements
Adaptive Logic:
  • Inverse relationship: Farther = brighter/louder, Closer = dimmer/quieter
  • Brightness: Linear mapping 30-100%
  • Volume: Steep curve (power 0.4) for noticeable changes
Stability Features:
  • Waits 1.5s for distance to stabilize
  • Movement threshold: 5cm resets timer
  • Grace range: ±10cm prevents micro-adjustments

## Slide 5: Phase 1 Features Completed
Core Functionality Delivered
✅ Distance-based Brightness Control
✅ Distance-based Volume Control with Steep Curve
✅ Presence-based Media Pause/Resume (3s timeout)
✅ Face Detection with MediaPipe Face Mesh
✅ Stability Logic for Crowd Scenarios
✅ Grace Range to Prevent Constant Adjustments
✅ Clean Console Output (Suppressed Warnings)
✅ Python 3.10 Compatibility with MediaPipe

## Slide 6: Code Structure & Organization
Clean, Modular Python Implementation
src/config/settings.py - Centralized configuration
src/modules/perception/ - Face detection & counting
src/modules/adaptation/ - Brightness & volume controllers
src/modules/intelligence/ - Environment & audio analysis
src/core/system_manager.py - Main orchestration
src/main.py - Clean startup with logging control

## Slide 7: Challenges Overcome
Technical Hurdles & Solutions
Python Version Compatibility:
  • MediaPipe 0.10.9 requires Python ≤3.11
  • Solution: Created Python 3.10 virtual environment
Stability in Crowd Scenarios:
  • Constant adjustments with moving crowds
  • Solution: Stability timer + grace range + movement threshold
Console Output Management:
  • MediaPipe INFO messages cluttering output
  • Solution: Suppressed logging to WARNING+ level
Volume Control Sensitivity:
  • Linear volume changes barely noticeable
  • Solution: Implemented steep power curve (0.4)

## Slide 8: Demo & Validation Results
System Performance & Behavior
✅ System starts cleanly with clear status messages
✅ Face detection works reliably with MediaPipe Face Mesh
✅ Brightness adjusts smoothly based on distance
✅ Volume changes noticeably with steep curve
✅ Media pauses after 3s absence, resumes on return
✅ Stability logic prevents erratic adjustments in crowds
✅ Grace range eliminates micro-adjustments
✅ Console remains clean during operation

## Slide 9: Future Development Roadmap
Phase 2-6 Expansion Plans
Phase 2: Gesture Integration
  • Hand detection and gesture-to-action mapping
  • Thumb-index distance for volume, wrist position for brightness
Phase 3: API + Dashboard
  • FastAPI backend with live metrics
  • React dashboard with face counting display
Phase 4-6: Enterprise & Public Display Features
  • Crowd analysis, weather adaptation, energy optimization
  • Security monitoring, analytics, edge deployment

## Slide 10: Conclusion & Achievements
Phase 1 Success & Next Steps
🎯 Phase 1 Objectives Met:
  • Core adaptive functionality implemented and tested
  • Robust distance-based controls with stability features
  • Clean, maintainable codebase ready for expansion
🔧 Technical Excellence:
  • Proper virtual environment management
  • Modular architecture for easy feature addition
  • Comprehensive error handling and logging
🚀 Ready for Phase 2: Gesture recognition integration